## Slide 1: Embedded Systems (Software)
Kavi Arya
CSE Dept.
IIT-Bombay

## Slide 2
From computers to embedded & networked SoCs … IoT
Complete change in device interaction
Growing number of critical applications
Beware of the computer!

## Slide 3: Computing without Computers (or, the changing nature of computers or, where/what is hardware?)

## Slide 4: Computing without Computers*
Changes in how we design/ deliver compute power
  Reconfigurable computing and custom computing
  i.e. turn sw into hw =>speed up (no single processor to slow us)
  Multi-core chips
Today’s computer chips surrounded by other cores
  Graphics processing, display handling, network interfacing, sound generation, wireless comm., etc.
  Supported by a range of functions embedded in hardware.
*Prof. Ian Page, University of Oxford, 1990’s

## Slide 5: Changes Happening
New ways of designing/delivering computer capability
  PCs, mobile phones, etc.
  Microsoft gaming sensor Kinect to become eyes/ears of robots
Changing structure of electronics & computing industry
  Largest manufacturer of cameras?
Changing products that people buy as well as the way that they buy and use them
  Tape-recorder -> Walkman -> digital players -> iPod -> …
  Books -> ebooks -> …
  Mainframe -> minicomps -> PCs -> servers -> cloud -> services
Changing how money made out of delivering value to customers
  Products changing into services
  Potentially deep & far-ranging effects of energy use & sustainability

## Slide 6: Technological & economic drivers of change
Nature of silicon industry
Extraordinary consequences of Moore’s Law.
Focus moving away from ASIC (application specific chip) technology towards standard chip products and thus lower prototype costs
Big winner: reconfigurable hardware - in particular FPGA chips
Can reduce the $6M development cost of a new chip to a few dollars and a few days

## Slide 7: Internet of Things (IoT)

## Slide 8
Internet of Things
The Shape of Things to Come… IoT

## Slide 15
Soon there will be no maids!! Then What?

## Slide 18
IoT & Analytics being fueled by Technology Advancements

## Slide 20
IOT/Analytics =>
massive amounts of data /traffic
1 ZB =
109 TB

## Slide 21
Personal (devices worn by consumers)
  Use cases: Wellness/ fitness monitoring, smart baby monitor, etc.
Home (devices in homes)
  Use cases: Home automation, energy management, connected security, etc.
Automotive (In cars/ light trucks interacting w/consumers)
  Use cases: In-vehicle infotainment (IVI), Advanced Driver Assistance Systems (ADAS), remote access, telematics, etc.
Healthcare (Systems/ devices for patient, provider, payer value chain)
  Use cases: Trial monitoring, personalized medicine, etc.
Building, Retail, Infrastructure, …
Relevant across all Industry Segments

## Slide 22
Increase reliability of operations
Increase QoS or product
Increase asset productivity
Increase workforce productivity
Increase customer satisfaction to reduce costs
Improve time to market
Reduce waste/cost of materials
New insights…
IOT for cost savings + revenue generation

## Slide 23
Cost & complexity:
  “Smart” lamps, thermostats, bulbs, …
Environmental Cost:
  E-waste, batteries, products with limited lifespan,…
Security:
  Fails due to shoddy engg.,
  Tesla-S buffer overflow
  Amazon Ring camera
Privacy:
  “Free” means that usage data is being monetized
Battery life:
  Wireless communication is generally very expensive!
Network:
  Typical COTS internet-enabled solns use 3G/4G, WiFi, BLE
  Except for BLE, unacceptably power hungry at the edge
IOT Problems

## Slide 24
Disruption good for entrepreneurs
Entrepreneurs embedded in opportunity
We need to train students with skills
HOW ??
IoT brings Disruption

## Slide 25: What is Internet of Things (IoT)?
Image courtesy: Google image
Analog
Digital
I2C, UART,SPI, etc..
SD Card
Drive
MQTT
CoAP

## Slide 26: Embedded System Diversity

## Slide 27: Common Design Metrics
NRE (Non-recurring engineering) cost
Unit cost
Size (bytes, gates)
Performance (execution time)
Power (more power=> more heat & less battery time)
Flexibility (ability to change functionality)
Time to prototype
Time to market
Maintainability
Correctness
Safety (probability that system won’t cause harm)

## Slide 28: Challenges
Tolerance for defects
Development Cycles
Resource availability
Ability to manage reqs
Ability to ensure long term maintenance
…Decreasing
Increasing…
Safety critical requirements in
  Aerospace & defence, Energy Transportation, Industrial, Medical
Requirement changes, life span
Application complexity
Cost of code testing, validation & verification & certification
Need for systems & software design reusability
Packaging & ergonomics are key
Mechatronics
Mass deployment – less scope for error
Mission & Safety-Critical Pressures

## Slide 29: Current Technology
Extrapolation of traditional software techniques
Programs written in conventional languages
  C subsets, MISRA C for automobile
  Java for telephone / smartcards
Glued together by OS services
  A wide variety of embedded OS (VxWorks, OSEK)
With some reuse and standardisation effort
Classical software models largely inadequate
  Too powerful, hard to verify
  often subsets of rich languages=>doesn’t make them simpler

## Slide 30: Why Is Embedded Software Not Just Software On Small Computers?
Embedded = Dedicated
Interaction with physical processes
  Sensors, actuators, processes
Critical properties are not all functional
  Real-time, fault recovery, power, security, robustness
Heterogeneity
  Hardware/software tradeoffs, mixed architectures
Concurrency
  Interaction with multiple processes
Reactivity
  Operating at the speed of the environment
These features look more like hardware!
Notes: Another definition for embedded systems:
  Embedded = dedicated
  Fixed functionality – No general purpose
  Fixed in Hardware

## Slide 31: Current Bottleneck
Intrinsic application complexity grows rapidly
  Analog / digital interface: more objects to control
  Embedded algorithmics: signal, display, alarm, power...
  Richer hardware architecture: P, DSP, ASIP, ASIC, FPGA
Performance adds complexity
  Footprint / power minimization interferes with logical design
  Technology independence is still difficult
=> Verification bottleneck
  Applications hard to verify off-site
  Hardware / software interaction difficult

## Slide 32: Apple A.. SoC series
Apple A4 (2010)
  for iPad ARM based SoC @1GHz w/integ. GPU ($1Bn to devlp)
Apple A5 (2012)
  Based on dual-core ARM Cortex-A9 MPCore CPU
  $4B development facility by Samsung in Texas
  Clocked at 1 GHz (auto adj. frequency to save battery)
  ISP for face detection, wh.balance & automatic image stabilization
  ”EarSmart" unit from Audience for noise canceling
  CPU portion 2x as powerful as the original iPad
  GPU up to 7x as powerful A4
  Cost 75% more than predecessor
Apple A6x (2013)
  1.4 GHz Apple-designed ARMv7 based dual-core CPU (Swift)
  Integrated quad-core PowerVR SGX 554MP4 GPU @300 MHz
  2x computing power + graphics perf. Of previous Apple A5X
  32 nm process => chip is 123 mm2 large[6] (26% larger than A6).
Notes: Refresh

## Slide 33
Year | Model | Specs | Product | Spd | Gfx | Size | Tech.
2012 | A6 | 1.3 GHz ARMv7 based dual-core CPU (Swift) | iPhone5 | 2x | 2x | 22% smaller | 32nM
2013 | A7 | 1.3–1.4GHz 64-bit ARMv8-A dual-core CPU (Cyclone) integrated PowerVR G6430 GPU, 31x64bit GP regs, 32x128bit FP regs | iPhone 5S, iPad Mini2 & 3 | 2x | 2x | 1B transistors in 102sq.mm | 28nM
2014 | A8 | 1.4GHz 64-bit ARMv8-A dual-core CPU & integrated PowerVR GX6450 GPU | iPhone6 & 6+ | 25% | 50% | 13% less in size, 2B transistors 89sq.mm | 20nM
2015 | A9 | 64-bit ARM based system on a chip (SoC) | iPhone 6S & 6S+ | 70% more | 90% more |  | 14nM
(Apple) Processor Trends

## Slide 34
Year | Model | Specs | Product | Spd | Gfx | Size | Tech.
2016 | A10 | 64-bit ARMv7 based SoC quad-core CPU (Fusion) | iPhone 7 | 40% faster | 50% faster | 3.3B transistors | 16nM
2017 | A11 | 64-bit ARMv8-A 6-core CPU (Bionic) 2 high perf and 4 high efficiency | iPhone 8 | 25% faster | 70% faster | 4.3B transistors | 10nM
2018 | A12 | 64-bit ARM 2+4 core CPU (Bionic) | iPhone XS & XR | 35% faster | 95% faster multi core | 6.9B transistors | 7nM
2019 | A13 | 64-bit ARM 6 core with 2 high perf cores running at 2.65GHz (Lightening) with ML accelerators – AMX blocks; & 4 energy efficient cores (Thunder) | iPhone 11 | 20% faster with 30% less pwr | 20% faster with 40% lower pwr | 8.5B transistors | 7nM
(Apple) Processor Trends

## Slide 35: Software Engineering (or, how do we build reliable systems?)

## Slide 36: Things Have to Change!
Pressure on productivity of design engineers working on complex systems.
Time has come to design hardware using software engineering - rather than hw engg - methodologies.
Complexity of system is the basic problem, and Moore’s Law doubles complexity every 18 months.
Advances in software engineering help produce complex systems with more easily available design skills, making large profits
We expect new designers, with/without hardware design skills, will design hardware in future

## Slide 37: Designer Productivity
“The Mythical Man Month” by Frederick Brooks ’75
More designers on team => lower productivity because of increasing communication costs between groups
Consider 1M transistor project: - Say, a designer has productivity of 5000 transistor/mth - Each extra designer => decrease of 100 transistor/mth productivity in group due to comm. costs
  1 designer 1M/5000 => 200mth
  10 designer 1M/(10*4100) => 24.3mth
  25 designer 1M/(25*2600) => 15.3mth
  27 designer 1M/(27*2400) => 15.4mth
Need new design technology to shrink design gap
Source: Embedded System Design: Frank Vahid/ Tony Vargis (John Wiley & Sons, Inc.2002)
Notes: Refresh

## Slide 38: Design Productivity Gap
Designer productivity grown over the last decade
Rate of improvement has not kept pace with the chip-capacity growth
1981: leading edge chip:
  100 designers * 100 trans/mth => 10k trans complexity
2010: leading edge Intel chip using 45nM technology:
  > 1B transistor complexity
2015: Leading edge Apple A9 using 14nM technology:
  > 2B transistor complexity
2019: Apple A13 chip using 7nM technology:
  > 8.5B transistor complexity
Designers at avg. of $10k pm => cost of building leading edge chips has gone from $1M (1981) to $300M (2002) to $1B (2010) to …
Apple A4 for iPad ARM based SoC @1GHz w/integrated GPU ($1Bn to develop)
Need paradigm shift to cope with complexities
Source: Embedded System Design: Frank Vahid/ Tony Vargis (John Wiley & Sons, Inc.2006)
And others.
Notes: Refresh

## Slide 39: Chip Design Cost

## Slide 40: Time to Market Design Metric
Simplified revenue model
  Product life = 2W, peak at W
  Time of market entry defines a triangle, representing market penetration
  Triangle area equals revenue
Loss
  The difference between the on-time and delayed triangle areas
Avg. time to market today = 8 mth
1 day delay may amount to $Ms
  see Sony Playstation vs XBox
On-time Delayed
entry entry
Peak revenue
Peak revenue from delayed entry
Market rise
Market fall
W
2W
Time
D
On-time
Delayed
Revenues ($)
Source: Embedded System Design: Frank Vahid/ Tony Vargis (John Wiley & Sons, Inc.2002)

## Slide 41: Losses due to delayed market entry
Area = 1/2 * base * height
  On-time = 1/2 * 2W * W
  Delayed = 1/2 * (W-D+W)*(W-D)
Percentage revenue loss = (D(3W-D)/2W2)*100%
Try some examples
On-time Delayed
entry entry
Peak revenue
Peak revenue from delayed entry
Market rise
Market fall
W
2W
Time
D
On-time
Delayed
Revenues ($)
  Lifetime 2W=52 wks, delay D=4 wks
  (4*(3*26 –4)/2*26^2) = 22%
  Lifetime 2W=52 wks, delay D=10 wks
  (10*(3*26 –10)/2*26^2) = 50%
  Delays are costly!
Source: Embedded System Design: Frank Vahid/ Tony Vargis (John Wiley & Sons, Inc.2006)

## Slide 42: NRE and unit cost metrics
But, must also consider time-to-market
Compare technologies by costs -- best depends on quantity
  Technology A: NRE=$2,000, unit=$100
  Technology B: NRE=$30,000, unit=$30
  Technology C: NRE=$100,000, unit=$2
Source: Embedded System Design: Frank Vahid/ Tony Vargis (John Wiley & Sons, Inc.2002)

## Slide 43: Software Engineering… Why we need it?

## Slide 44: Enemy number 1 : the bug
Therac 25 : lethal irradiations
Dharan's Patriot
Ariane V
Mars Explorer, Mars Polar Lander
High-end automobile problems
Pentium, SMP cpu networks
Telephone and camera bugs
Bugs grow faster than Moore's law!

## Slide 45: Other Important Issues
Hardware / software partitioning
  Hardware / software source code independence
  Link between programming and performance analysis
Operating Systems / scheduling
  Well-studied field: rate-monotonic, earliest deadline first, etc.
  Newer computation models need less explicit scheduling
Fault tolerance
  Software redundancy, voting algorithms, etc.
  CRCs, TT networks

## Slide 46: How to avoid or control bugs?
Traditional : better verification by fancier simulation
Next step : better design using specific techniques
  Better and more reusable specifications
  Simpler computation models, formalisms, semantics
  Reduce architect / designer and customer / provider distance
  Reduce hardware / software distance
Requires better tooling
  Higher-level models and synthesis
  Formal property verification / program equivalence
  Certified libraries

## Slide 47: Anatomy of Embedded Applications
CC : continuous control, signal processing
  Differential equation solving, filters
  Specs and simulation in Matlab / Scilab, manual or automatic code
FSM : finite state machines, state transition systems
  Discrete control, protocols, networking, drivers, security, etc.
  Flat or hierarchical state machines, manual or automatic code
Calc : calculation intensive
  Navigation, security, etc.
  C, manual + libraries
Web : web-like navigation, audio / video streaming
  Consumer electronics, infotainment systems
  Data-flow networks, embedded Java

## Slide 48: BMW 745i : Prelude To Complexity
Another Life Cycle Example : The Software Error

## Slide 49: External view
Rough running engine, possibly stall
Severity: 6 incidents in 5,470 cars with 2 rear endings
  “alleged injury” of BMW passengers
  Fault of drunk or inattentive following drivers
  “Engine malfunction,
  drive with moderation”
The problem: software error, a desynchronization
of the valvetronic motors

## Slide 50: BMW Cost
To repair: Reprogram ECU
Recalls not uncommon in industry
  BMW 5,470 cars @ $68,500 = Rev $372 mil
Compare Cost: Recall BMW X5
  164,000 units @ $66,800 = Rev $10 bil.
  ~$5 Million
  ~$30 per SUV

## Slide 51: Bosch EMU For Four Wheeler ( Multi Cylinder)
Source: Bosch Brochure : Ref 6

## Slide 52: Design Issues (How do we build these systems?)

## Slide 53: Functional Design & Mapping
HW1
HW2
HW3
HW4
Hardware Interface
RTOS/Drivers
Thread
Architectural Design
F1
F2
F3
F4
F5
Functional Design
(F3)
(F4)
(F5)
(F2)
Source: Ian Phillips, ARM
VSIA 2001

## Slide 54: Synchronous languages
Started in the 80's
  Esterel : Ecole des Mines / INRIA, SyncCharts : U. Nice
  Lustre : IMAG, Signal : INRIA Rennes
  Lava : Chalmers, Xilinx
Started in the mid-90's
  Handel-C: University of Oxford, Celoxica Inc.
Industrial use in the 90's
  Lustre / SCADE : nuclear plants (Schneider), avionics (Airbus)
  Esterel : avionics (Dassault), telecom
=> Full development in the 2000's
  avionics: Airbus, Dassault, Elbit, Eurocopter, SNECMA, Thales,...
  automotive: AUDI, GM, PSA,...
  hardware pilot projects / experiments: TI, STM, Xilinx, Intel, Thales
Notes: Drop

## Slide 55: Trends
Moore’s Law
  IC transistor capacity doubles every 18 mths
  1981: leading edge chip had 10k transistors
  2002: leading edge chip has 150M transistors
  2010: Leading edge Intel processor has 0.5B trans in 107sq.mm
  2014: Leading edge Intel processor has 2.0B trans in 89sq.mm
  2019: Leading edge Intel processor has 8.5B trans in 83sq.mm
  Why? reducing trans size, increasing chip size, clever circuits
  Changing due to paradigm shifts: sys design tools, nanotech, ...
Designer productivity has improved due to better tools:
  Compilation/Synthesis tools
  Libraries/IP
  Test/verification tools
  Standards
  Languages and frameworks (Handel-C, Lava, Esterel, …)
  1981: designer produced 100 transistors per month
  2002: designer produces 5000 transistors per month
  2020: designer produces ???
Notes: Drop?

## Slide 56
Design of Solutions
Investigation
Modern Tool Usage
Individual & Team Work
Communication
KNOWLEDGE OR SKILLS REQUIRED
How do we get there?

## Slide 58: Academic Program (Minor?)
M.Tech. Course:
  CS684 Embedded Systems (Software) / Sem 2
  Background required: Basic understanding of Operating Systems at UG level C programming
Related courses:
  EE617 Sensors in Instrumentation / Sem 1
  EE616 Electronic System Design / Sem 1
  EE712 Embedded Systems Design / Sem 2
CS684: Takeaways
  Insight into system design for embedded/ time-critical apps
  The satisfaction of building (hw/sw) system to solve a problem

## Slide 59: Guidelines (CS684)
Compulsory Labs (on Wed):
  7 labs (introduction to Embedded Systems)
Compulsory Workshop (on 2 Sat):
  Introduction to IoT System Building
Evaluation
  10% Quiz, 10% Assignments, 10% 2 weekend wkshp, 10% Wed. labs, 40% Project (with 10% project-based endsem/individually assessed), 20% Midsem
  Surprise quizzes
  Percentages may be tweaked as we progress
  Project seeded pre-midsem, implemented post midsem

## Slide 60: Course Details (No Audit)
Mail ids:
  Moodle based interaction with TAs
  Faculty: kavi@cse.iitb.ac.in
Assignments
  On Moodle - subscribe to 'CS 684' on Moodle
  http://moodle.iitb.ac.in
Lab team:
  Lohit, Kalind, Rutuja, Omkar, Kedar
Workshop Team:
  Lohit, Omkar, Avijit, Vikrant, Andrea, Rutuja
CS684 TA:
  Diptesh Kanojia (Lead TA) diptesh@cse...

## Slide 61: Microcontroller Labs
Dates:
  Wednesdays (beginning 22nd Jan., Intro on Thu. 16 Jan.)
Introduction to Microcontroller concepts
  Intro to Atmega2560, Peripherals and Visual Studio Code
  Understanding GPIO and Peripherals of Atmega2560
  Interrupts/Timers, PWM and Servo Motor Interfacing
  Introduction to RTOS using ESP32 Microcontroller
  ADC/Interfacing Joystick
Applications:
  Automation
  IoT

## Slide 62: Conclusion
We have simultaneous optimisations of competing design metrics: speed, size, power, complexity, etc.
We need a “Renaissance Engineer”
  w/holistic view of design process & comfortable with technologies ranging from hw, sw to formal methods
Maturation of system-building tools
  Enables unified view of hardware/ software co-design.
Design efforts focus at higher levels of abstraction => Abstract specifications refined into programs then into gates and logic.
There is no fundamental difference of between what hardware and software can implement.